## Slide 1: Sentinel Turret Rover: Intruder Defense System with Precision Shooting
Team-B12
Abhishta H Mallaya - CB.AI.U4AID23102 Gowtham S D - CB.AI.U4AID23113 Kanishka S J - CB.AI.U4AID23121
Vyshnav kumar S - CB.AI.U4AID23151

## Slide 2
Contents
Introduction
Objective Methodology
Hardware Software Communication
Results

## Slide 3: Introduction
Traditional surveillance relies on fixed cameras and passive monitoring.
These methods lack real-time response and adaptability.
AI-driven security systems can autonomously detect, classify, and respond to threats. Sentinel Turret Rover: A dynamic, AI-powered mobile security system.

## Slide 4: Objective
Development of a mobile robot with a turret mounted on it
Obstacle Detection by the mobile robot
Training a model to classify the faces of the allies
Intruder Detection by setting a probability score as threshold obtained by the model Send real-time alerts (image + notification) to security personnel.

## Slide 5: Methodology
Hardware Components - Chasis
Mobile robot chasis DC Motors Ultrasonic sensor L298N Motor Driver

## Slide 6: Methodology
Hardware Components - Turret
Turret Body (Assembled 3D printed parts) MG-90 Servo Motor
L298N Motor Driver Arduino Nano
9V - 6.5V Buck Coverter

## Slide 7: Methodology
Hardware Components - Control
Raspberry Pi 5 is used to control both the chassis and the turret using the Serial module available in Python.
It also runs the code for real time classification using the model trained.

## Slide 8
Methodology
Hardware: Sentinel Turret Rover

## Slide 9: Methodology
Software Pipeline
Step1: Data Preprocessing
Face cropping using DLib Face detector Splitting into training and testing data
Augmenting training data to reach a specified no.of samples
Step2: Model Training Step3: Real Time Testing

## Slide 10: Methodology
Data Augmentation Pipeline
Resize
Random Horizontal Flip Random Rotation
Random Aﬀine Transformation (rotation, translation, scaling) Color Jitter (brightness and contrast)
Gaussian Blur Noise Injection

## Slide 11: Methodology
Model Architectures Used
CNN with CBAM (Convolutional Block Attention Module)
CNN with CA-CBAM (Cross Attention Convolutional Block Attention Module) CNN with ArcFace CA-CBAM
YOLO based Self Attention

## Slide 12
Methodology
CBAM (Convolutional Block Attention Module)

## Slide 13: CA CBAM (Cross Attention Convolutional Block Attention Module)
Methodology

## Slide 14
Methodology
ArcFace CA CBAM

## Slide 15
Methodology
ArcFace CA CBAM

## Slide 16: Alert System
A Telegram bot is created and integrated with Python code, which performs real-time classification
and triggers the bot to send live notifications to the user via Telegram.
Python requires the BOT_TOKEN and CHAT_ID as follows:
BOT_TOKEN = '8111117866:AAGZI-zZLwbaGVqAIfzKlXclJobiMPtcZe0'
CHAT_ID = '6855415361'
These values are used to send alerts when an intruder or ally is detected.
18 / 26

## Slide 17: Methodology
Alert System
If an intruder is detected:
Intruder detected!
Otherwise:
Ally detected!
18 / 26

## Slide 18
Methodology
Alert System Working Mechanism

## Slide 19
Results & Discussion
Training & Validation loss: CNN with CBAM

## Slide 20
Results & Discussion
Training & Validation loss: CNN with CA CBAM

## Slide 21
Results & Discussion
Training & Validation loss: CNN with ArcFace CA CBAM

## Slide 22: Training & Validation loss: YOLO based Self ATTENTION
Results & Discussion

## Slide 23: Results & Discussion
Model Performance Comparison
Model
Table: Classification Accuracies of Different Models
Training Acc. (%) Testing Acc. (%)
CBAM | 99.00 | 97.50
CA-CBAM | 95.38 | 92.50
ArcFace CA-CBAM | 97.75 | 95.00
YOLO-Self Attention | 94.30 | 93.80

## Slide 24
Results & Discussion
Notification Log from the Telegram Bot

## Slide 25
Results & Discussion
Coordinates Calculation for shooting

## Slide 26: Results & Discussion

## Slide 27: Results & Discussion
The system captures a person’s face through the webcam and classifies it into one of the predefined classes, displaying the predicted class along with the probability and bounding box coordinates on the image and distance between the turret and person along with their coordinates.
If an intruder (unknown person) is detected, the turret automatically aligns itself to the detected coordinates and initiates the firing sequence.
Simultaneously, an alert message is sent to the designated recipient using the specified BOT_TOKEN and CHAT_ID.

## Slide 28: Future improvements
Lack of quality of camera
Portability issues
Improve shooting range
Model training efficiency can be improved